Timer Instructions
(Flasher)

  The first ting to do if you haven't already is to download the files for the circuit board and upload them to your PCB manufacturer of choice. I use PCB Way (Not Sponsored) but there are others.

You will also need;
- 2 x Duel (2 Way) PCB mount Screw Headers at 5.08mm Pitch. Jaycar Part Number HM3172.
- 1 x NE555P Timer Integrated Circuit or similar (555 Timer). Jaycar Part Number ZL3555.
- 2 x 1K Ohm ¼ Watt Resistors.(1/2 Watt OK). Jarcar Part Number RR0572.
- 1 x 470K Ohm ¼ or ½ Watt Resistor. Jaycar Part Number RR0636.
- 1 x 2n222 NPN Transistor TO-92 Package. Any General Purpose Switch type Transistor with Collector pin 1, Base Pin 2, and Emitter Pin 3 will do.
- 1 x .68uF Electrolytic Capacitor.
- 1 x .1uF Ceramic or similar capacitor.

  Assembly is straight forward with all the components and position information included on the Board.

  Enjoy, and please let me know if you make one,
Cheers
Mark